## Slide 1: Resource Capacity Values and Power Supply Adequacy
Technical Conference on Capacity Planning and Resource Adequacy
John Fazio and Ben Kujala
NW Power and Conservation Council
Helena, Montana
June 8, 2017

## Slide 2: Integrated vs. Standalone
Integrated capacity value equals the standalone value plus capacity gained from the interaction with hydro storage
During off-peak hours1, non-hydro resources can generate instead of hydro, which saves water and increases hydro’s peaking capacity
1If applicable, prices permitting.

## Slide 3: Why Integrated Capacity is Higher Using Hydro Storage to Increase Capacity
Chart: Hour of Day
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Orig | 15000 | 15000 | 15000 | 15000 | 15000 | 15000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 25000 | 15000 | 15000
w/INC + DEC | 12000 | 12000 | 12000 | 12000 | 12000 | 12000 | 26500 | 26500 | 26500 | 26500 | 26500 | 26500 | 26500 | 26500 | 26500 | 26500 | 26500 | 26500 | 26500 | 26500 | 26500 | 26500 | 12000 | 12000
Increases hydro peaking by 24,000 MW-hours or 1,500 MW/hour over 16 peak hours.
Replace hydro generation during off-peak hours with other generation to save 24,000 MW-hours or 3000 MW/hour over 8 off-peak hours.
Blue Curve = Before
Red Curve = After

## Slide 4: Standalone and Integrated Capacity Values using Gorge Wind
Standalone Capacity | Added Wind |  | 3000 | MW
 | Reduction in MW needed for adequacy |  | 90 | MW
 | Standalone Capacity = 90/3000 |  | 3.0 | %
Integrated Capacity | Added Wind |  | 3000 | MW
 | Reduction in MW needed for adequacy |  | 286 | MW
 | Integrated Capacity = 286/3000 |  | 9.5 | %

## Slide 5: 7th Power Plan ASCC Values (relative to nameplate capacity)
Resource | Q1 | Q2 | Q3 | Q4
Solar PV | 0.26 | 0.81 | 0.81 | 0.42
Energy Efficiency1 | 1.24 | 1.01 | 1.14 | 1.16
Gorge Wind | 0.03 | 0.11 | 0.11 | 0.08
Gas-Fired Turbine | 1.28 | 1.00 | 1.02 | 1.20
Geothermal | 1.28 | 1.00 | 1.02 | 1.20
1The “nameplate” capacity value for EE is roughly estimated to be 1.9 times the energy savings during winter and 1.2 times the energy savings in summer. The ASCC values are applied to the “nameplate” capacity value for EE to get the integrated capacity value.

## Slide 6: 2021-22 Adequacy Summary1
2021 LOLP = 6.9%
  Boardman, Centralia 1 and N Valmy 1 plants retire (1,457 MW)
  New load forecast shows lower winter peaks
  New Canadian operation increases US hydro generation in summer but lowers hydro generation in October
  New assumption – add spot market access in October
  Reduced balancing reserves slightly increase hydro sustained peak
2022 LOLP = 7.2%
  Colstrip 1 and 2 and Pasco plants retire (352 MW)
  317 aMW of EE and 100 aMW of codes & standards savings
Effective Capacity Needed in 2021 ≈ 400 MW (adding 400 MW in 2021 also covers the adequacy need in 2022)
1LOLP values and needed capacity can change significantly depending on future demand and Southwest market availability.

## Slide 7: 2022 LOLP Heat Map
 | Winter Spot Market |  |  | 
Load | 3400 | 3000 | 2500 | 2000
High | 18.1 | 19.0 | 21.0 | 23.6
Med | 5.8 | 6.2 | 7.2 | 8.6
Low | 1.8 | 2.1 | 2.7 | 3.4

## Slide 8: 2022 Capacity Needed (MW)
 | Winter Spot Market |  |  | 
Load | 3400 | 3000 | 2500 | 2000
High | 1500 | 1600 | 1830 | 2100
Med | 115 | 200 | 385 | 650
Low | 0 | 0 | 0 | 0

## Slide 9
Chart: Projected Installed Nameplate of Coal Generators Serving the Region
| 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Current | 7434.165 | 7434.165 | 7179.905 | 5848.915 | 5848.915 | 5132.115 | 5132.115 | 5132.115 | 4135.125 | 4135.125 | 4135.125 | 3557.25 | 3557.25 | 3557.25 | 3557.25 | 2979.375 | 2979.375 | 2979.375 | 2979.375
7th Plan (Feb 2016) | 7434.165 | 7434.165 | 7434.165 | 6103.175 | 6103.175 | 6103.175 | 6103.175 | 6103.175 | 4851.925 | 4851.925 | 4851.925 | 4851.925 | 4851.925 | 4851.925 | 4851.925 | 4851.925 | 4851.925 | 4851.925 | 4851.925