## Slide 1: Response Comments
Technical Conference on Capacity Planning and Resource Adequacy
Montana Public Service Commission
Helena, Montana
June 8, 2017
  Arne Olson, Partner

## Slide 2: High level comments on Power Council Presentation
Benefits of hydro/gas/wind coordination are real – John did the math right!
Very difficult to get these synergies without regional coordination –
  Bonneville is not going to build the wind or the gas
Effective MW are lower if calculations are done alone
  Potential for tens or even hundreds of million in annual savings from regional resource adequacy
Energy efficiency that contributes to peak has higher value
Region appears to need new resources in 2021-2022 – not clear whether replacements will be built in time
Value of lost load: intuitive to bend the demand curve, however VOLL is not well understood

## Slide 3: Average vs. Marginal Capacity Value
The portfolio capacity value is the most relevant calculation to consider in resource planning
  Due to the complementarity of different resources the portfolio value will be higher than the sum of each individual resource measured alone
  It is sometimes necessary to attribute the capacity value of the portfolio to individual resources
    There are many options, but no standard or rigorous way to do this
The marginal capacity value, given the existing portfolio, is more appropriate for use in procurement
  This value will change over time as the portfolio changes
Chart: 
 | 40 | 100
 | 40
Individual Solar Capacity Value
Individual Wind Capacity Value
Combined Capacity Value

## Slide 4: What are the potential savings from regional resource adequacy?
 | Northwest |  |  | Southwest | 
 | BPA Area | NWPP |  | AZ-NM-NV | WestConnect
Individual Utility Peak + 15% PRM | 33,574 | 46,398 |  | 35,459 | 57,270
Regional Peak + 15% PRM | 32,833 | 42,896 |  | 34,474 | 54,597
Reduction (MW) | 741 | 3,502 |  | 985 | 2,673
Savings ($MM/year) | $89 | $420 |  | $118 | $321
Regional Peak + 12% | 31,977 | 41,777 |  | 33,575 | 53,173
Reduction (MW) | 1,597 | 4,621 |  | 1,884 | 4,097
Savings ($MM/Year | $192 | $555 |  | $226 | $492
Calculated based on hourly loads from 2006-2012
Assumes capacity cost of $120/kW-yr.
Assumes no transmission constraints
Some savings already being achieved

## Slide 5: High level comments on NWE presentation
Someone will need to build capacity to meet the regional needs
NWE is probably the most vulnerable of NW utilities to shortage conditions
If the flexible capacity cost premium is high, NWE could investigate dispatch of wind to help reduce flexibility needs
  Cost of compensated curtailment compared against cost premium of flexible capacity
  Pre-curtailment can preserve resources to provide inc resource
  Wind and solar can be placed on AGC

## Slide 6: Things I forgot to say
Firm resources need firm fuel supply
  For gas resources, firm transportation contracts or dual-fueling capability

## Slide 7: Thank You!
Energy and Environmental Economics, Inc. (E3) 101 Montgomery Street, Suite 1600 San Francisco, CA 94104 Tel 415-391-5100 Web http://www.ethree.com
Arne Olson, Partner (arne@ethree.com)